## Slide 1: Designing Printed Circuit Boards – PADS Layout Flow
Yousef Shakhsheer
yousefshak@gmail.com
Robust Low Power VLSI Group

## Slide 2: Revision History
Revision History | Date | Reviser | Notes
1.0 | 4/30/12 | Yousef Shakhsheer (yas5b) | 
2.0 | 5/27/13 | Divya Akella (dka5ns) | Changed slide order, added some additional info on assigning pcb decals, multi-planes and copper pour

## Slide 3: Overview
This tutorial is intended to get people started with the PADS flow.
We use PADS Logic 9.3.1 for schematics and PADS Layout 9.3.1 for PCB layout for this tutorial.

## Slide 4: Layout

## Slide 5: Outline
Layout
  Creating footprints
  Connecting footprints to parts
  Creating Board Layout
  Autorouter

## Slide 6: Libraries
The libraries we create in PADS schematic and layout are seen by both tools
Since in a previous tutorial we created a library (see Schematic tutorial) we can simply add the library here (library manager tool stays the same between schematic and layout)

## Slide 7: Add a Library

## Slide 8: Use “Manage Lib. List” then click “add” and locate the library to add it to PADS

## Slide 9: PCB Decals
We can now add a decal to the library we imported
PCB decals are the footprints that will appear on the board for components
Decal Entry and Footprint Production
Datasheet
Design tool
Fabrication

## Slide 10: Create a new PCB decal in the library
While still in the library manager (from adding the library we created previously) click the “New…” button to add a new decal

## Slide 11: From the part data sheet we find the suggested layout
NOTE THAT EVERYTHING IS DONE IN MILS = .001”
(it is also common to see mm here so double check all physical drawings)

## Slide 12: Open the drafting toolbar to begin drawing your part
Drafting Toolbar
CAE Decal Wizard

## Slide 13: Decal Wizard
Notice control of dimensioning, handy to avoid a bunch of unit conversions here
Decal parameters
A number of common pin configurations are available

## Slide 14: Once complete save the decal and return to the parts editor
Hit no if you already have a schematic symbol.
Notes: TODO:
Add a slide showing the output in the parts editor form the decal wizard

## Slide 15: Assigning PCB decal to its schematic Part
Go to Library Manager -> Parts -> Edit

## Slide 16
Edit Electrical -> Select the Decal -> Assign

## Slide 17: Go back to your schematic (from previous tutorial)
You need to ensure that each part has a part decal.
Right click on the part -> Edit electrical (from menu bar) -> PCB decal and select your decal
Re-export your netlist
Keep your schematic open (this is where dual-monitors is helpful)
Notes: -Show the affiliation of parts with decals

## Slide 18: Layout
The layout describes the physical orientation of traces and components on the board
The layout takes as its input the netlist from the schematic entry tool and automatically imports the corresponding PCB footprints from the library (if available)

## Slide 19: Open up a new layout and import the netlist
File -> Import
Select your netlist (tutorial.asc). You’ll see components get imported in.

## Slide 20: Let’s make life easier
You can link your schematic and layout editor together
Make sure both your schematic and layout are open
Tool -> Pads Layout or click the “Link to” button in the top right corner
Now if you click on a component or a node in layout, it will be highlight in the schematic and vice versa.
NOTE: This does not mean that any netlist changes (such as adding a part or deleting a connection in the schematic) will be reflected in the layout (look at ECO control for this)

## Slide 21: Disperse the components
Tools
->
Disperse Components
Spreads the components out for easy viewing and selection

## Slide 22: Drawing a 2”x2” board outline
NOTE THAT EVERYTHING IS DONE IN MILS = .001”.
This give you the length of the line.

## Slide 23: The Origin
In all physical design we need some point to reference all positions relative to, we call this point the origin
The origin may not be set close to the board outline we just created
Though it may not be too helpful for us in this tool-flow having the origin near, or within, the board margins is desirable

## Slide 24: Let’s change the origin
Setup
->
Set origin
Click on the left bottom corner of the board outline and click okay.

## Slide 25: Design Rules
Now that we have our components and origin setup we will want to lay out some basic rules for design
Common rules enforced are:
  Max/min trace width
  Min spacing for traces and vias (through-holes)

## Slide 26: Let’s set the design rules
Setup-> Design Rules
You should check the advanced circuits website to see what the minimum specs are for PCB design
We are only concerned with the “Clearance” section under “Design Rules”

## Slide 27: Clearance and Width Suggestion for Typical Signal Trace
You have the ability to set things for individual nets. On the previous slide, hit nets instead of general. For VDD and GND, you want to set recommended trace to at least 10 mils.

## Slide 28: Dynamic Rule Checker (DRC)
The DRC allows us to automatically check any trace routing or part placement we are taking part in as we are doing it
The DRC engine can thus prevent us from creating placements or signal paths that violate a set of predetermined ground rules

## Slide 29: Let’s turn on the DRC
Tools-> options
Hit design on the left
Turn on DRC (design rule checker) – prevent errors
This will prevent you from making stupid mistakes.
YOU WILL HAVE TO CHECK BACK PERIODICALLY TO ENSURE THIS IS ON. WHEN YOU RESTART THE PROGRAM THIS DEFAULTS TO OFF

## Slide 30: Change the grid
The grid is the set of points on which we draw our design, often finer resolution for this grid is desired
Change the design grid, via grid, and fan out grid (as shown in the figure).
Uncheck snap to grid only for VIA grid.

## Slide 31: Set the number of layers
Setup -> Layer Definition
The default is a two layer board. You can change this by hitting the modify button.
To create voltage planes, you need to associate it a layer. To do this click on the layer (aka Bottom), change the plane type to split/mixed and then click on the Assign Nets button and select the net aka (GND) and add it.

## Slide 32: Placing components on the board
Right click and select “select components”
Drag them on to the cut out.
You can rotate by right clicking on the component and on “Rotate 90 degrees” or by hitting Ctrl+r

## Slide 33: Helpful tips
Each color corresponds to a layer. You can change these colors through: Setup->Display Colors
You view specific layers by selecting it on the menu bar
You can place components on the top and bottom layer. To change the side of a component, right click on the component and hit “flip”.

## Slide 34: Board Documentation
Like all technical works PCBs are documented
This documentation occurs in a layer referred to as the silkscreen (since it is adhered to the solder-masked PCB via a silkscreen process)
When using Advanced Circuits solder-mask and silkscreen errors are generally not significant (they are automatically resolved before production)
Silkscreen Documentation is extremely important
Use Silkscreen Top or Silkscreen Bottom layers for this purpose. Make sure you flip the text in Silkscreen Bottom (check Mirrored), so that it is readable from the bottom plane.
It is important to document because it tells you which resistor is which so spend time on it.

## Slide 35: Let’s move some documentation
Right click anywhere and choose “Select documentation”
Click the documentation you want to move and drag it to a convenient place
Good
Bad

## Slide 36: Change the via shape
For many applications the default via is too large
Press F2 (to enter the trace routing mode) and click on a pad
Draw a wire out a bit, then right click and select “add via”
Right click again and click on end
Or just use Ctrl+Left Click shortcut to drop a via in place

## Slide 37: Editing Vias
Hit escape to exit the routing mode
Right click “Select Pins/Vias/Tacks”
Click on the via to highlight it, right click on it, and select “properties”.
Click on the Pad Stack

## Slide 38: Changing the Via Pad Stack
The pad stack represents the interaction of the pad with each of the subsequent PCB layers
Editing the pad stack allows us to change the via’s pad diameter (its metal outline) and drill size
Some smaller via reference settings:
  Diameter: 27 mil
  Drill Size: 15 mil

## Slide 39: Signing the board
You will have to turn off the DRC to edit the silkscreen.
Select “Silkscreen Top”
Change the size/width
End result:

## Slide 40: Copper Pours (Planes)
The X means that it will be tied to a plane (which we defined earlier). We need to pour a copper plane.
A copper plane lies in a layer of the PCB and provides a large contact area for vias and/or traces to connect (Vdd and GND are commonly used planes)

## Slide 41: Performing Copper Pours
Turn DRC back on, if it isn’t already
If you need to flood a GND or the Voltage plane after Autorouting, you will need to create the outline before Autorouting. For this
Set the layer you want to make the pour in on top
Hit the copper pour button and create a polygon around where you want to pour copper.

## Slide 42: Performing Copper Pours
Select desired layer for the pour (in this case: bottom)
Select desired net for the pour (in this case: GND)
Hit okay to create the pour
NOTE: This will not fill the pour, only create the fill outline on the PCB

## Slide 43: Autorouting
Turn on DRC
Tools -> Pads Router
Hit proceed
A new program will open up.

## Slide 44: Autorouting
Tools -> Autoroute -> Start
You’ll see your board routed
Always look at your output window to see if all traces were routed
If everything looks alright, hit tools-> verify design.
Save and quit this router. Open up the file in Pads Layout.

## Slide 45: Filling Copper Pours
Hit the flood button and touch one of the sides of your copper plane
Hit okay. You should get something like this.
Alternatively: use the “Fast Flood” option to fill all pours at once

## Slide 46: Design Verification
We can now verify that our design passes all the rules set earlier
We can check:
  Clearance: The space between parts/vias/traces is sufficient
  Connectivity: The drawn traces correspond exactly to those indicated in the netlist
  Fabrication: Common design flaws. Principally acid traps, which occur where a PCB trace achieves an angle of less than 90 degrees with an incident face. This may result in etchant being trapped in the corner through washing and corresponding degradation (along with possible failure) of the connection later on
  Other fabrication tests may yield silkscreen or solder-mask errors which can be ignored.

## Slide 47: Running Verification
Tools -> Verify Design
Ensure you can see the whole board.
Do the following tests:
  Clearance
  Connectivity
  Fabrication (only worry about acid trap errors)
Correct any errors and run tests iteratively until there are no relevant failures

## Slide 48: You’re done!
See the PADS CAM Export and DFM submission tutorial for affiliated output file generation and board submission